## Slide 1: Automotive CAN Node for Smart Defogging and Adaptive Headlight Control
Guided by: | Submitted by:
 | Name: K. Dhanashree PRN: 250240130009
 | Name: U. Poonam PRN: 250240130024
 | Name: R. Vaishnavi PRN: 250240130029
 | Name: D. Sakshi PRN: 250240130030
 | Name: A. Shivangi PRN: 250240130034

## Slide 2: Problem Statement
Problem 1: Fog-Induced Visibility Obstruction Fog forms on the windshield due to temperature & humidity difference. Manual defogging distracts the driver and delays response time.
Need: Automatic detection of high humidity & activation of defogger.
Problem 2: Improper Headlight Usage Drivers forget to switch headlights in low-light conditions (tunnels, dusk, fog). Unnecessary high-beam use causes glare to oncoming traffic.
Need: Intelligent detection of ambient light & vehicle distance for adaptive headlight control.

## Slide 3: Objectives
Sensor Integration
Real-time Data Processing
CAN Communication Implementation
Adaptive Headlight Control
Smart Defogging System

## Slide 4: HC-SR04 Ultrasonic Sensor
Purpose:
Proximity detection of oncoming vehicles
Principle:
Time-of-flight of 40 kHz ultrasound
Specs:
Range: 2–450 cm
Trigger: 10 µs TTL pulse
Echo: pulse width 4 m distance
Integration:
TRIG/ECHO to STM32 GPIO, input capture

## Slide 5: DHT11 Temperature & Humidity Sensor
Purpose:
Detect cabin humidity & temperature for fog-risk assessment
Principle:
Resistive humidity + NTC thermistor
Specs:
Humidity: 20–90% RH ±5%
Temp: 0–50°C ±2°C
Integration:
Single-wire + pull-up resistor

## Slide 6: Light Dependent Resistor (LDR)
Purpose:
Detects ambient light for headlight control.
Principle:
Resistance decreases as light intensity increases.
Specs:
High resistance in dark, low in light
Integration:
Uses a voltage divider circuit to give ADC an input.

## Slide 7: 3-Axis Accelerometer (LIS3DSH)
Purpose:
Detect vehicle motion/tilt
Principle:
Measures acceleration using MEMS capacitive sensing.
Specs:
- has a 16-bit ADC for high resolution
- a Digital Motion Processor (DMP) for data fusion.
Integration:
Connects to STM32 via SPI protocol and is interrupt-based.

## Slide 8: CAN
A CAN network is a system network made up of CAN node ( electronic control units with a CAN interface) which exchange data with another over their individual CAN interfaces and a transmission medium (CAN bus) that interconnects all the CAN interfaces.
Why CAN?
Robustness and Reliability
Real-Time Communication
Multi-Master Architecture
Efficiency
Widely Supported
CAN Protocol in Automotive Industry
Used due to Reduced Wiring, Robust in noisy environments, Real- Time performance, Scalability and Interoperability
Application using CAN: Engine Control, Transmission Control, Anti-Braking System, Body Control, Airbag Control Module
CAN Bus Type: High Speed CAN(up to 1Mbps), Low Speed CAN(~125 kbps), CAN FD(up to 8Mbps)
Future Aspects : Automotive Ethernet

## Slide 9: CAN Controller Network Communication in Project

## Slide 10: System Block Diagram

## Slide 11: Circuit Diagram

## Slide 12
Conclusion
Robust sensor integration via CAN for safety.
Functional Adaptive Headlight Control
Effective Smart Defogging System
Future Enhancements
• Replace DHT11 with DHT22
• ECU integration & in-vehicle testing
• Add rain/lightning sensors for full adaptability

## Slide 13: Thankyou